## Slide 1: EPA Perspective on ISO 17025 Accreditation
Tony Dolan OEE, Air Enforcement Unit
01 June 2011
Notes: <number>

## Slide 2: Topics to be addressed
EPA thinking behind mandatory accreditation
Auditing of air Contractors against EPA Guidance notes
Main benefits of accreditation- consistency, quality, & level playing field.
Notes: Stack testing in Ireland prior to 1994 was confined mainly to those sites that were licensed under the Air Pollution Act 1987.
The responsibility for monitoring rests, in the first case, with the licensed operator. This is referred to as self-monitoring.
The licence document stipulates the frequency of monitoring and often allows for the scope of the monitoring to be altered with the approval of the Agency.
Quality of data: Very important area, as the results generated on site must be representative of what was actually happening on site at the time of sampling,
Accreditation of stack samplers: Tech Spec 15675. ISO 17025: is an elaboration of ISO 17025 (fixed labs) with partic ref to stack testing contractors.
These two standards (TS 15675, EN15259) together form an accredit/certification system which is very similar to the MCERTS system in UK.
<number>

## Slide 3: Why introduce mandatory accreditation?
AG2 issued as best practice, but not mandatory.
2009 workshop – feedback was for mandatory system
Review of practice in other EU countries in 2010
  UK, Spain, France, Netherlands, Denmark, Germany
  Findings: accreditation is mandatory for IPPC monitoring
Issues identified when auditing monitoring reports
Need for increased confidence in results
Industrial Emissions Directive – much stronger emphasis on the application of BAT.
Need to provide transparent and quality driven services

## Slide 4: Process to Date
Release of AG2 (best practice, but not mandatory requirement)
October 2009 workshop discussion
EPA: review of practice in other countries and development of proposed plan
  EPA Board Approval
  Issue of circular e-mail to licensees in December 2010
  Circular letter also sent to monitoring contractors for information
  Notification to IBEC
  Liaison with INAB and their appointed contractors
  Commencement of limited scope of auditing licensee contractors
  Proposal for mandatory accreditation from January 2014
  Air workshop June 2011

## Slide 5: Process from 2011 to 2014
Commencement of accreditation process
Close interaction between INAB and EPA during initial stages of accreditation process
Develop policy for in-house monitoring
Liaison with contractors/Env. Services Association (ESA)
Ongoing auditing of licensee self monitoring – site visits and document review
INAB/EPA workshop in 2012 and 2013 to assess progress?
Maintain good communications/feedback between all parties to ensure the process is inclusive.

## Slide 6: Topics to be addressed
EPA thinking behind mandatory accreditation
Auditing of air Contractors against EPA Guidance notes
Main benefits of accreditation- consistency, quality, & level playing field.
Notes: Stack testing in Ireland prior to 1994 was confined mainly to those sites that were licensed under the Air Pollution Act 1987.
The responsibility for monitoring rests, in the first case, with the licensed operator. This is referred to as self-monitoring.
The licence document stipulates the frequency of monitoring and often allows for the scope of the monitoring to be altered with the approval of the Agency.
Quality of data: Very important area, as the results generated on site must be representative of what was actually happening on site at the time of sampling,
Accreditation of stack samplers: Tech Spec 15675. ISO 17025: is an elaboration of ISO 17025 (fixed labs) with partic ref to stack testing contractors.
These two standards (TS 15675, EN15259) together form an accredit/certification system which is very similar to the MCERTS system in UK.
<number>

## Slide 7: Quality of emissions data
Notes: Describes all the key elements of a successful monitoring campaign.
This Air Monitoring Guidance Note (AG2) aims to summarise the many aspects of stack emission monitoring that contribute to the quality of the data.
Test houses (stack testing contractors) should have regard to this guidance note however it is only the first level of documentation that they must consult if they are to provide a good quality service.
For Site managers: this guidance note should serve as a useful reference source to ensure the objectives of their monitoring programmes are met.
The basic layout of the guidance note is as set out above.
<number>

## Slide 8: Reference Documents
The EPA Air Guidance notes on Sampling facilities (AG1), and on Air Monitoring (AG2).
CEN standards such as TS 15675, and EN 15259,
  TS 15675: provides for application of ISO 17025 to periodic stack testing.
  EN 15259: specifies requirements for monitoring platforms/locations, & for planning, and reporting of emissions at industrial plant.
Standard Reference methods for the relevant parameters for particulates, gases, moisture, dioxins.
Relevant Procedures
A copy of the IPPC licence

## Slide 9: On Site Assessment
Risk Assessment: EPA check with the Air Contractor that the RA is completed before going up to the stack, see section 6 of AG1.
Platform Inspection Cert (GA3): A copy of this form will be given to the site contact to fill out. See section 3.1 of AG1
Pre site meetings with Env. manager, and the Air contractor are very useful to explain the process & get relevant feedback.
  Need to review H&S issues, hazards, PPE, & evacuation procedure etc. with the Env. manager to complete our own Risk Assess.
Site Specific Protocol: Will review the SSP & compare against App 5 of AG2.
  Process details, substances to be monitored, expected emission values, measurement methods, equipment to be used etc.
Notes: Technical Specification: TS 15675: 2007 provides for the application of ISO 17025 to periodic stack test measurements, & will provide basis for the accreditation of test houses by INAB.
EN 15259: 2007 Specifies the requirements for monit platforms/locations and requirements for determining the monit objectives, planning monit campaigns and reporting of emissions, and supporting measurements at sites.
TS 15675. ISO 17025: is an elaboration of ISO 17025 (fixed labs) with part reference to stack testing contractors.
These two standards (TS 15675, EN15259) form an accredit/certif system which is very similar to the MCERTS system in UK.
INAB certification: accreditation of labs under ISO 17025
Hope to role out the accreditation to all sectors over time (not just WID, & LCPD sites).
<number>

## Slide 10: Hazards associated with stack monitoring

## Slide 11: Some Initial Observations
Tidiness & layout of the of the van – ex. equipment & glassware stored in suitable containers.
Qualifications & experience of the air sampling team
  1 man teams are not recommended unless the monitoring is very straightforward or a buddy system is in place (heavy equipment).
Sampling train leak test: should include a dry gas metre (to record flow), or can use a rotameter if it has been traceably calibrated.
Field blanks: should be included as part of the leak check, analytical blanks also required for ex. particulates (use control nozzle & filter in the lab).
Documentation on site: Should have the relevant documents (Risk assessment, SSP, Standards, & procedures) for review on site.
  Standards can be available in CD form

## Slide 12: Observations (cont’d)
Certified Gas: All span gases used on site should be compared against a certified gas back in the laboratory.
Span: should use a zero & span to check for instrument drift.
  Should span through the probe tip (systems check), and through the analyser, & record the instrument drift (2-5% allowable).
Oxygen: the oxygen conc. is used to calculate the gas density, which is used to calc the gas velocity (when measured using a Pitot static tube).
The water vapour content of the gas is also used in the calculation, use gravimetric method with balance & weights.
Measurement uncertainty: the estimation of uncertainty is a requirement of the relevant CEN standards (section 4.3, and 8.5.3 of AG2).

## Slide 13: Topics to be addressed
EPA thinking behind mandatory accreditation
Auditing of air Contractors against EPA Guidance notes
Main benefits of accreditation- consistency, quality, & level playing field.
Notes: <number>

## Slide 14: Requirements for Licencees
Need to ensure that quality is the underlying objective
Need to pay a suitable fee, and make an assessment on the competency (or otherwise) of the air contractor.
  Qualifications & experience of the air contractor.
  Equipment used: should be using certified equipment.
  Span gases: should be using a zero & span gas on instruments etc.
Don’t accept shortcuts on either H&S or the monitoring programme.
Responsibility rests with the licencee to ensure that results are reliable and robust.
Poor quality reports will not be accepted by the EPA (min. of AG2 requirements). We will carry out regular spot checks.

## Slide 15: Air monitoring checklist for licensees
Prior to Site Visit:
Has contractor provided details on qualifications, training and relevant experience?
Has contractor inspected sampling location and assessed suitability?
Does the service agreement/contract meet the requirements of AG2?
On-Site:
Has contractor developed a Site Specific Protocol for the scope of work?
Has contractor requested details of process conditions that day?
Has all portable monit equipment been calibrated, & are certs available?
Is the method used in line with licence requirements, or AG2?
Notes: Has the proposed contractor provided evidence/details of their qualifications, training and experience in carrying out stack emissions monitoring, with particular reference to the scope of work to be completed.
Has monitoring for all necessary supporting parameters (e.g. oxygen level, stack gas velocity, temperature, moisture, pressure) been carried out?
Is the contractor familiar with the requirements of the licence in terms of supporting parameters required (do they have a copy of the licence)?
For any portable analysers, how are the data being logged? Is periodic data also being logged manually in case of data logger failure?
<number>

## Slide 16: In-house monitoring teams
Personnel certification: is considered to be a minimum requirement for the in-house air sampling team.
  This may suffice if there is a small scope of monitoring, or the in-house expertise is well established
  If trained staff leave then the IPPC site cannot carry out the monitoring!
Ideally should look at moving towards ISO 17025 accreditation, or consider contracting out the work from 2014 onwards.
  Full accreditation would need to be considered where a site is carrying out an extensive scope of monitoring.

## Slide 17: Role of EPA/ESA
EPA
  Liaise with INAB during development of accreditation process and on an ongoing basis;
  Interaction with licensees on relevant issues
  Provision of support to contractors where possible, e.g. PT scheme
  Evaluate certification/accreditation process w.r.t. in-house monitoring
  Interaction with ESA
ESA may play an important role in reducing potential costs?
  Coordinate training, continuing professional development
  Representative body for interaction with INAB/EPA
  Representative body for interaction with licensees
  Coordinate PT scheme

## Slide 18: Main Benefits – EPA, Air Contractors, & Licencees
Everyone is working to the same standard, as otherwise we would have market distortion
The quality should improve, but time and costs required to carry out a successful monitoring campaign will increase.
Easier to audit monitoring reports
Agency may look at reducing monitoring frequency provided the site are compliant and data is considered to be reliable
A recognition that the no. of air sampling organisations may reduce given the significant resources required!
This is a time consuming and expensive process but is a mandatory requirement and has received Board approval.
Recognition of personal expertise.

## Slide 19: In summary
Accreditation to ISO 17025 for field operators is now officially underway.
Applications should be submitted to INAB.
EPA will continue to carry out audits of air contractors against the AG2 requirements.
EPA to liaise with INAB on developing a policy for in-house monitoring
Will continue to liaise with contractors/Env. Services Association (ESA)
Additional workshops in 2012 and 2013 to assess progress
Would expect an ongoing improvement in quality of air monitoring, but time and costs required to carry out a successful monitoring campaign will increase.
Notes: It is important that the licensee is somewhat familiar with methods used, complexities involved, potentials for error and with quality requirements of monitoring and reporting.
In the licensees interests to take an interest in the work of contractors. Need also to be aware of licence requirements on competency as presented by Ken.
Don’t be afraid to ask questions of your own contractors or of the EPA contractors when they visit your site.
<number>