## Slide 1: In-house Air Monitoring at IPPC Facilities – An Operator’s Perspective
Simon Barry (Manager, Thermal Performance)
John Gilmartin (Lead Technologist)
ESB Energy International,
Generation Operations
1 June, 2011

## Slide 2: Agenda
Background & History of ESB Air Monitoring
CEMS Management
Quality Air Monitoring
Typical Work & Practicalities
ISO 17025

## Slide 3: ESB Thermal Generation Portfolio
Poolbeg
Gas / Gas oil
CCGT
Aghada
Gas / Gas oil
CCGT / OCGT / Thermal
Marina
Gas / Gas oil
OCGT
Moneypoint
Coal / HFO
PF
Lough Ree Power
Peat / Biomass
Fluidised Bed
West Offaly Power
Peat / Biomass
Fluidised Bed
North Wall
Gas / Gas oil
CCGT / OCGT
7 Thermal Sites
Capacity ~2850MW
Range of Technologies
Fuels
  Gas
  Coal
  Peat
  HFO
  Gas Oil

## Slide 4: ESB Air Monitoring Background
ESB Test & Efficiency Department
Since 1960’s – Flue gas testing for thermal plant
Early 90’s – NOX emissions (Moneypoint low NOX)
Late 90’s – CEMS installation (Opsis) & testing
2005 ~ Now – EN14181 compliance
2006 – VGB Emissions Monitoring Working Group
Current team (Thermal Performance) – 3 persons

## Slide 5: ESB, Quality & EN14181
EN14181:2004 Stationary Source Emissions – Quality Assurance of Automated Monitoring Systems
CEMS Quality Assurance Development
2004: Monitoring compliance for LCPD & EN14181
2005 – EN14181 planning & implementation
2006 – VGB European Working Group on EN14181
2006 – Marina QAL2 (first ESB EN14181 test)
2006~2007 – EPA AG3 steering group
Members of Source Testing Association
Interface to VGB / EOn / EDF

## Slide 6: CEMS Management
Local Management
ISO14001 Certification
Central Support Functions
  Environmental
  Testing / Thermal Performance
Expertise increases CEMS
  Quality
  Availability
  Reliability
Station
Environmental
Coordinator
Station
EI&C
Technicians
Central
In-house
Testing
Central
Expert
Functions
OEM
Service
& Parts
Work
Management
System
Environmental
Management
System
CEMS

## Slide 7: CEMS Quality Assurance
EN14181
EN14181
EN14956
Manufacturer
Operator / Test House
Operator / Test House

## Slide 8: ESB Air Monitoring Quality Assurance
Equipment
  Certification
  Calibration
  Traceability
Methods & Procedures
Standard Reference Methods
Internal Auditing
Competence & Training
  (MCERT’s)
Objective
Reporting
Quality

## Slide 9: Typical ESB Air Monitoring Work
Plant Emissions Validation & Acceptance Testing
CEMS Cross Checks
Abatement Plant Optimisation
Thermal Performance Optimisation
EN14181 Compliance
  QAL2
  Annual Surveillance Tests
Other
  CEMS Expert Advice & Troubleshooting
  Witness CEMS Acceptance Testing

## Slide 10: Testing Equipment
Range of Species Monitored for Compliance
  NO & NO2
  SO2
  CO / CO2
  Particulates
Equipment
  Extractive Heated Line
  Chiller Dryer
  Horiba PG250 & Eco-Physics
  Tecora Iso-kinetic & Gravimat
  Electrochemical (MRU)
Certified Calibration Gases (UKAS)

## Slide 11: Emissions Testing – Amorebieta, Spain

## Slide 12: Moneypoint MERP Acceptance Testing
Witness & Test Coordination
Moneypoint Environmental Retrofit Project

## Slide 13: EN14181 Compliance
Poolbeg CCGT
Aghada CCGT
Lough Ree Power

## Slide 14: Some Technical Challenges…
UKAS Certified Calibration Gases
NOX Converter Efficiency > 95%
Blocked Heated Lines & Probes
QAL3 Process Automation
Plant Dispatch

## Slide 15: Practicalities – Getting the Test Done
Plant Dispatch by Eirgrid National Control Centre
National electric demand = supply in real time
Wide variability in dispatch, difficult to predict (wind generation)
Specific load @ specific times = difficult!
In-house test team = flexible
Flexibility to react to plant dispatch reduces :
  Environmental impact
  Test cost (€€€)

## Slide 16: Practicalities – Plant Dispatch
Dispatch effects test window

## Slide 17: Quality management
Quality Management System (e.g. ISO 17025)
ESB has Quality Management:
  Significant Experience & Competence
  Certified Equipment & Reference Materials
  Calibration & Testing Procedures
  Auditing
  External Training & Certification (UK MCERTs)
  Reporting

## Slide 18: Difficulties with ISO 17025 Implementation
Thermal Performance – small team (3)
Significant workload in setting up for ISO 17025
Additional workload in managing ISO 17025 QMS
Resources & €€€!
More suited to larger laboratory environment
No economy of scale for ESB
Decision – business case for accreditation?

## Slide 19: Benefits of In-House Testing to ESB
Expertise in business critical area
Flexibility
Ownership of issues
Familiarity with installation & equipment
Allows us to challenge manufacturers and 3rd party tests
Reduced
  Environmental impact
  Testing cost
Focus
  getting job done right
  not quickly => quality benefits
In house monitoring => best fit

## Slide 20: Summary
Background
CEMS Management
Quality Processes
Typical Work & Challenges
ISO 17025
Benefits of In-house Monitoring to ESB

## Slide 21: Questions & Answers
In-house Air Monitoring at IPPC Facilities -
An Operator’s Perspective
Simon Barry & John Gilmartin
ESB Thermal Performance
simon.barry@esb.ie