## Slide 1: The end of the start – catchment characterisation
Jenny Deakin, Marie Archbold and Donal Daly on behalf of the Catchment Science and Management Unit
With assistance from EPA colleagues and RPS consultants
Notes: Catchments Unit has been engaged in a comprehensive process of characterising every waterbody. Will summarise the national findings and look at how the information will be used in the next steps

## Slide 2: What is characterisation?
Is there a problem?
What is causing it, where, and why?
How do we fix it?
Must be evidence based
All recorded in the WFD Application

## Slide 3: Characterisation approach
Aiming for ‘The right measure in the right place’
Monitor
Status
For every waterbody…

## Slide 4
Risk assessment outcomes
(all water bodies)
Approximately one third (1360) of all waterbodies are At Risk of not achieving WFD objectives and need additional action
Risk

## Slide 5: P is the most significant WQ issue
Issues | Possible pressures
P – eutrophication (rivers/lakes) N – eutrophication (saline) | Agriculture, WWTPs, DWWTSs, Urban areas, Forestry, Industry
Ammonium | Peat extraction, WWTPs
Fine sediment | Channel maintenance, forestry, agriculture
Channel modification | Channel maintenance, drainage works
Industrial pollutants | Landfills, industry
But we need the significant pressures for each water body
Just come through a very comprehensive assessment process
Significant issue

## Slide 6
Half of all At Risk water bodies are impacted by multiple pressures
Significant Pressures in At Risk rivers and lakes (TraC/GW in progress)
Significant pressures

## Slide 7: How do we select the right measure?
We now have a better understanding for every waterbody:
  What the water quality problems are, where and why.
  Where to focus in to carry out field scale investigative assessments.
  What the biophysical characteristics are, as a basis for determining
  ‘the right measure in the right place’. Critical for diffuse pollution.
Investigative assessments are carried out on At Risk WBs:
  Catchment, stream and shore walks, focussing on significant pressures
  Rule areas in or out to target the effort
  Refine understanding of the problem to identify the right measure
  Resource intensive but very cost effective
  Eleven structured types that can be quantified for resource allocation
  Guidance currently being developed by a working group
Identifying multiple benefits will be important
Measures

## Slide 8: Challenges
There is a significant challenge to:
  Carry out all field scale investigative assessments
  Identify the right measure(s), e.g. awareness raising, engagement, change of practice, supports, enforcement
  Engage with the pressure owners and implementing bodies and Get the measure(s) implemented
  Capture the outcomes and track progress in a structured way
Measures
NB: Particularly challenging for diffuse problems such as agriculture (‘death by a thousand cuts’, multiple diverse land holders, multiple problems, multiple agencies/players, multiple messages, lack of resources on farm)
We won’t need ‘new’ measures everywhere
‘One size fit all’ approaches are not the solution.
Local specific advice critical

## Slide 9
Critical Source Areas now delineated
Map of relative risk of transport of diffuse P from agriculture to rivers via OF pathways
Not field scale. Field scale ‘investigative assessments’ needed to find the right solution
Pollution Impact Potential maps
Measures

## Slide 10
Currently developing the WFD App to record Investigative assessments
Measures

## Slide 11: Steps involved in setting Environmental Objectives
Technical –
  Risk, significant issues and pressures
  Management strategies, scenario analysis
  Draft RBMP Priorities
Public Agencies and Communities
  Measures planned or already initiated
  Community groups in place
  Resources
  Local priorities
Regional and National Priorities
  Coverage of settings/issues, multiple benefits
  Consider regional resources, development, future plans
  National policy – DHPCLG, WPAC, cost benefit.
Objectives
Regional technical workshops
Characterisation
Regional Committees
National committees Minister

## Slide 12
Regional workshop process
At Risk
Feasibility
Plan priorities
Other priorities, project recommendations
Objectives
Objectives depend on:
Regional workshop outcomes
Resources
Regional committee deliberations
Minister
Will be estimated to give overall planned outcomes when decisions are made (late 2017).

## Slide 13: EPA contribution to the final plan
  Complete all catchment assessments
  Work with LAWCO to deliver regional technical workshops
  EPA/LAWCO to report to Regional Committees on workshops
  Consider the implications of the decisions of the Regional Committees for the setting of environmental objectives for each water body
  Continue development of the WFD App and catchments.ie
  Review WFD monitoring programme in the context of new information
  Once plan is complete: report to Europe

## Slide 14: Is this going to work?
  Recognition that a clean, healthy environment has a marketing value
  Dairy Industry Initiative, pilot projects
  Acceptance that our heterogeneity means ‘one size does not fit all’
  Water and Communities Office set up, communities are engaging
  Business case for resources for ~50 extra staff for investigative assessments and follow up actions
  Good collaboration between Departments and Agencies
  Investment in data sharing, tools and catchments.ie
  Challenge now is to follow through and make it happen

## Slide 15
j.deakin@epa.ie