## Slide 1: 2024 SoE Report Water
Dr Wayne Trodd & Alan Stephens (EPA)
Co-authors: Paddy Morris, Dr Caroline Wynne, David Shannon, Ken Bucke, Dr Jenny Deakin (EPA)
State of the Environment Conference, Dublin 16th October 2024

## Slide 2: Introduction
Why is this important?
Water Quality - Explained
Current situation
Significant Pressures & Issues
Responses
Outlook
Key Messages

## Slide 3: Why is this important?
Water is essential to life.
‘Our rivers, lakes, estuaries, coastal waters and groundwaters sustain our livelihoods, food production and industries, support our tourism and recreational activities, and are an integral part of our culture and heritage. As well as being critically important to humans, water is just as essential for the many species that call Ireland’s waters home.’
We must protect and maintain the health of our waters.
‘Without clean and healthy waters, we cannot hope to sustain a vibrant society or a thriving aquatic environment with diverse species and habitats.’
Finny River, Co. Mayo. Hugh Feeley

## Slide 4: Water Quality – Explained
Ireland has an extensive water quality monitoring programme, undertaken by the EPA, local authorities, Inland Fisheries Ireland, Waterways Ireland and the Marine Institute. The EPA classifies and reports on the quality of surface waters (rivers, lakes, estuaries and coastal waters) and groundwaters every 3 years under the approach set out in the Water Framework Directive.
Water Quality 2019-2021 report
Water Indicators 2023 report.

## Slide 5: Water Quality – Explained
Black Valley – Ruth Little
Protect
Restore

## Slide 6: Current Situation Ecological Status (2019-2021) of Surface Waters
54% of our surface waters (rivers, lakes, transitional and coastal waters) are in High/Good status.
Estuaries currently have the worst water quality. Coastal waters have the highest percentage of waters in satisfactory condition.
Latest full assessment
Next full assessment in 2025

## Slide 7: Current Situation Chemical Status (2019-2021) of Surface Waters
Half of the surface waters monitored in the period 2016-2021 failed to achieve good chemical status due to the exceedance of environment quality thresholds for at least one hazardous chemical substance.
When ubiquitous substances (chemicals widespread in the aquatic environment, such as mercury) are excluded from the assessment, 88% of water bodies monitored are in good chemical status.

## Slide 8: Current Situation Status (2019-2021) of Groundwaters
With a few localised exceptions, the quality and quantity of groundwater in Ireland is generally good.
92% of groundwater bodies are in good chemical status
Over 99% are in good quantitative status.
Overall, 91% of groundwater bodies met both objectives, accounting for 97% of the country by area.

## Slide 9
Chart: Surface Water Ecological Status (Monitored Rivers, Lakes, Estuaries & Coastal)
| 2007-2009 (2480) | 2010-2015 (2682) | 2013-2018 (2717) | 2016-2021 (2737)
High | 329 | 289 | 230 | 268
Good | 1085 | 1202 | 1192 | 1121
Moderate | 676 | 714 | 777 | 847
Poor | 357 | 450 | 494 | 485
Bad | 33 | 27 | 24 | 16
Ecological status of monitored surface water bodies
2007-2021

## Slide 10: Significant Pressures
34% (1,649) of water bodies are at risk of not meeting their objectives. Action needed in all sectors:
Agriculture
Hydromorphological Pressures
Forestry
Urban Waste Water
Report: Update on pressures impacting on water quality available on EPA publications page https://www.epa.ie

## Slide 11: Significant Pressures
Agriculture (1023 water bodies) –Main issue is loss of nutrients. Sediments and hazardous chemicals also a problem.
Hydromorphology (448 water bodies) – Changes to the flow and physical habitat damage ecology and the natural processes and functions in water bodies e.g. drainage, channelisation and dredging.
Forestry (216 water bodies) - Activities such as afforestation, forest road works, thinning, clear-felling and reforestation can cause the release of sediment, nutrients and pesticides to water bodies and can impact habitat conditions.
Urban Wastewater (197 water bodies) - The main issues arising from urban waste water are the release of nutrients (nitrogen and phosphorus), organic pollution and the release of pathogens from poorly or untreated sewage that pose a risk to human health.

## Slide 12: Issues – Nutrients River Nitrate 2021-2023
Nitrate
42% of river sites have unsatisfactory nitrate concentrations (above 8 mg/l NO3)
No improvement

## Slide 13: Nitrogen in Estuaries and Coastal 2021-2023
17% of water bodies have unsatisfactory nitrogen concentrations.
Majority of these water bodies are in south and southeast.
No Improvement.
Inner Dundalk Bay- Wayne Trodd

## Slide 14
27% of river sites have unsatisfactory phosphate concentrations (above 0.035mg/l P)
No improvement
Phosphate
Phosphate in Rivers
2021-2023

## Slide 15: Total Phosphorus in Lakes 2021-2023
35% of lakes have unsatisfactory total phosphorus concentrations (above 0.025 mg/l P) .
Majority of these lakes are in the Border region.
No improvement.
L. Mask-Hugh Feeley

## Slide 16: Responses
Water Action Plan 2024 published in Sept. Blueprint by which Ireland addresses water quality issues. Needs to be effectively implemented and tracked.
Nutrient levels in our waters need to decrease.
We need targeted action. Measures need to be in the right place.
Full implementation of Nitrates Action Programme including compliance in the National Agricultural Inspection Programme.
Uisce Éireann need to continue to prioritise investment in areas where wastewater is impacting on water quality.
Community and stakeholder engagement is key.
Climate adaptation and water resilience need to be built in to plans.
Research and innovation e.g. Waters of LIFE; Farming for Water EIP

## Slide 17: Outlook
Gap analysis conducted by EPA on measures in the Water Action Plan 2024.
Focussed on 34% of water bodies at risk of not achieving objectives by 2027.
Significant challenge ahead to meet our water quality objectives.
150-300 water bodies forecast to meet water quality targets by 2027.
500–650 water bodies may see some improvements - measures in place by 2027.
864 water bodies do not have specific, targeted measures planned - therefore unlikely to achieve their status objectives by 2027.
583 water bodies - pressures not known.

## Slide 18: Key Messages
We need a reduction in nutrients (nitrogen and phosphorus) entering our waters. Nitrogen pollution is an issue especially in the south and south-east and needs to be reduced. Targeted measures to reduce phosphorus run off will also be beneficial.
We need to see full implementation of existing environmental legislation and high compliance rates across all regulated activities. Right measure in the right place.
Water governance structures need to be reviewed to ensure that they operate effectively. Need improved tracking of actions and progress in the Water Action Plan.
It is essential to build climate resilience into water quality management and water services.

## Slide 19: Thank You
Thanks to everyone who contributed to this chapter.
Thanks for listening.
Water quality data available on www.catchments.ie